## Slide 1
FPGA Development
Stages, Methods & Tools
A Comprehensive Guide for Complex SoC & FPGA Designs
Vendor-Agnostic | Engineering Manager Perspective

## Slide 2
Agenda
2 / 60
1
FPGA Architecture & Device Landscape
2
SoC Devices — Hard CPUs & Soft Cores
3
Key Subsystems: Transceivers, DDR, DSP, AI Engines
4
Development Flow Overview
5
RTL Design, IP Integration & Protocols
6
Synthesis, Implementation & Timing Closure
7
Pinout Planning & Power Design
8
Verification & Validation
9
Hardware Bring-Up, Debug & Production

## Slide 3
FPGA Architecture
Understanding the silicon building blocks
3 / 60

## Slide 4
What Is an FPGA?
4 / 60
Field-Programmable Gate Array
Reconfigurable silicon fabric that can be programmed and reprogrammed after manufacturing.
Unlike ASICs, FPGAs offer flexibility, parallelism, and rapid prototyping — ideal for complex, evolving designs.
Parallelism
Thousands of operations execute simultaneously
Reconfigurability
Reprogram in-field without respinning silicon
Time-to-Market
Weeks vs. months for ASIC tape-out

## Slide 5
FPGA Internal Architecture
5 / 60
CLBs / Logic Cells
LUTs, flip-flops, carry chains — the basic logic fabric
Block RAM (BRAM)
Distributed & block memory for on-chip storage
DSP Slices
Hardened multiply-accumulate units for math-intensive tasks
Clock Management
PLLs, MMCMs for clock synthesis, deskew, and domain crossing
I/O Banks
Configurable I/O standards: LVCMOS, LVDS, HSTL, SSTL, etc.
Transceivers (GT)
Multi-gigabit serial links: PCIe, Ethernet, Aurora, JESD204

## Slide 6
Modern FPGA Device Families
6 / 60
Vendor | Family | Target | Key Feature
AMD/Xilinx | Versal | Data Center, 5G | AI Engines + ARM + PL
AMD/Xilinx | UltraScale+ | HPC, Networking | HBM, 58G transceivers
Intel/Altera | Agilex 7/9 | Data Center, Mil | CXL, HBM2e, PCIe 5.0
Lattice | Nexus / Avant | Edge, Embedded | Low power, small packages
Microchip | PolarFire | Aerospace, Ind. | Radiation tolerant, low power
Efinix | Titanium | Edge AI | Quantum fabric, RISC-V
Trend: Modern FPGAs integrate hard processors, AI accelerators, and HBM — blurring the line between FPGAs and SoCs.

## Slide 7
SoC FPGA Devices
Hard processors, soft cores & heterogeneous compute
7 / 60

## Slide 8
SoC FPGAs — Hard CPU Subsystems
8 / 60
Processing System (PS)
Hardened ARM Cortex-A / Cortex-R cores embedded alongside the programmable logic (PL).
Includes: L1/L2 caches, interrupt controllers, DMA, on-chip interconnect (AXI), boot ROM.
Runs Linux, RTOS, or bare-metal firmware. The PS boots first and can configure the PL dynamically.
Key SoC Platforms
Zynq-7000
Dual Cortex-A9 + Artix/Kintex PL
Zynq UltraScale+ MPSoC
Quad A53 + Dual R5 + Mali GPU + PL
Versal Adaptive SoC
Dual A72 + Dual R5 + AI Engines + PL
Intel Agilex SoC
Quad A55 / A76 + PL + HPS
Microchip PolarFire SoC
RISC-V (4×U54 + 1×E51) + PL
PS ↔ PL interface is critical: AXI HP, AXI ACP, AXI GP ports determine bandwidth and coherency.

## Slide 9
Soft Processor Cores
9 / 60
Processors synthesized into programmable logic — flexible but consume FPGA resources.
MicroBlaze / MicroBlaze V
AMD/Xilinx
32-bit RISC, MMU optional, AXI interconnect, mature ecosystem
Nios II / Nios V
Intel/Altera
32-bit RISC / RISC-V, Avalon bus, Platform Designer integration
VexRiscv / PicoRV32
Open Source
RISC-V cores, highly customizable, community-driven
Cortex-M1 / M3 DesignStart
ARM
Licensed soft cores for FPGA prototyping, AMBA AHB/APB

## Slide 10
Key Subsystems
Transceivers, DDR, DSP, protocols & AI engines
10 / 60

## Slide 11
High-Speed Transceivers (SerDes)
11 / 60
Multi-gigabit transceivers (MGTs) enable serial links from 1 Gbps to 112+ Gbps per lane.
Critical for PCIe, Ethernet, JESD204B/C, Aurora, SATA, DisplayPort, and custom protocols.
TX/RX Architecture
PCS + PMA layers: encoding (8b/10b, 64b/66b), CDR, equalization (DFE, CTLE), pre-emphasis
Protocol Support
PCIe Gen3/4/5, 10G/25G/100G Ethernet, JESD204B/C, Interlaken, CPRI/eCPRI, SRIO
Design Challenges
Eye diagram tuning, jitter budgets, channel loss compensation, reference clock planning
Debugging
IBERT / Transceiver Toolkit loopback tests, PRBS pattern generators, eye scan

## Slide 12
DDR Memory Interfaces
12 / 60
External memory is essential for data-intensive FPGA applications.
Aspect | Details
Standards | DDR3, DDR4, DDR5, LPDDR4/5, HBM2/2e (high-end)
Controller IP | Hard MIG (Xilinx), EMIF (Intel), or soft controllers
Calibration | Write/read leveling, DQS gate training, VREF training — automated by IP
Key Constraints | Impedance matching, fly-by topology, VTT termination, PCB trace length matching
Bandwidth | DDR4-3200: ~25.6 GB/s (64-bit), HBM2e: ~460 GB/s aggregate
Verification | Memory model simulation (Micron VIP), hardware eye scans, stress tests

## Slide 13
Digital Signal Processing on FPGAs
13 / 60
Hardened DSP Slices
DSP48E2 (Xilinx) / DSP Fixed-Point (Intel) blocks provide:
27×18 multiplier + 48-bit accumulator + pre-adder
Pipelining registers for high clock rates (>500 MHz)
Pattern detect, SIMD modes, cascading chains
Used in FIR/IIR filters, FFTs, matrix operations
DSP Design Approaches
HDL (RTL)
Manual instantiation for max control
HLS / Model-Based
C/C++, MATLAB/Simulink → HDL
Vendor IP Catalog
FIR Compiler, FFT, DDS, CORDIC
Custom Pipelines
Chaining DSP slices for throughput
Typical DSP applications: radar, SDR, image processing, telecom baseband, audio, medical imaging.

## Slide 14
AI Engines & Specialized Compute Units
14 / 60
Next-generation FPGAs embed hardened AI accelerators alongside traditional PL.
Versal AI Engines
Array of VLIW + SIMD vector processors, 400+ AI-TOPS INT8, connected via NoC
Versal AI Edge
AI Engine-ML tiles optimized for edge inference workloads, lower power
Intel AI Tensor Blocks
Agilex-embedded blocks for INT8/FP16 inference acceleration
Lattice sensAI
Edge AI stack for Nexus/Avant: CNN accelerator IP + quantization tools
Design flow: Vitis AI / oneAPI frameworks compile DNN models → graph partitioning → AI Engine kernels + PL datapath.

## Slide 15
Complex Protocols & IP Core Ecosystem
15 / 60
PCIe Gen3/4/5
DMA subsystems, BARs, MSI-X, root complex / endpoint modes
100G Ethernet
MAC + PCS, RS-FEC, AXI-Stream interface, timestamping for PTP
JESD204B/C
ADC/DAC interfacing for RF systems — deterministic latency, multi-link sync
DDR/HBM Controllers
Hard or soft MIG/EMIF with calibration, ECC, and reordering
AXI Interconnect
On-chip bus fabric: AXI4, AXI4-Lite, AXI4-Stream — the backbone of SoC integration
MIPI CSI-2 / DSI
Camera and display interfaces for embedded vision
IP integration strategy: Buy vs. build vs. open-source — evaluate licensing, support, and verification readiness.

## Slide 16
Development Flow
From specification to bitstream
16 / 60

## Slide 17
FPGA Development Flow — Overview
17 / 60
1
Requirements
& Spec
→
2
Architecture
& Partitioning
→
3
RTL Design
& IP Integration
→
4
Functional
Verification
→
5
Synthesis &
Implementation
→
6
Timing
Closure
→
7
Bitstream &
Validation
Iterative Process
Each stage may loop back: timing failures trigger re-synthesis, verification bugs require RTL changes, pinout constraints affect floorplanning.
For SoC designs, add parallel software development tracks (firmware, drivers, OS bring-up) and HW/SW co-verification.

## Slide 18
Requirements & Specification
18 / 60
Functional Spec
Define I/O interfaces, data rates, latency budgets, processing functions, and control protocols
Device Selection
Logic density, DSP/BRAM counts, transceiver speeds, I/O count, thermal envelope, package & cost
Architecture Partitioning
PS vs. PL split (SoC), clock domains, memory hierarchy, inter-block interfaces
Constraint Specification
Target Fmax, pinout pre-planning, power budget, environmental (temp, vibration)

## Slide 19
RTL Design & HDL Languages
19 / 60
Hardware Description Languages
SystemVerilog
Industry standard — RTL + verification (UVM)
VHDL
Strong typing, common in aerospace & defense
Chisel / SpinalHDL
Scala-based HDL generators for parameterized designs
HLS (C/C++/OpenCL)
Algorithm → RTL: Vitis HLS, Intel HLS, Catapult
MATLAB/Simulink HDL Coder
Model-based design → synthesizable HDL
Best Practices
Synchronous design methodology
Parameterized, reusable modules
Clock domain crossing (CDC) awareness
Reset strategy: sync vs. async, per-domain
Coding for synthesis: infer RAMs, DSPs correctly
Lint checks: Spyglass, Ascent, Questa Lint
Version control: Git + CI/CD pipelines

## Slide 20
IP Core Integration Strategy
20 / 60
Source | Examples | Pros | Cons
Vendor IP | MIG, PCIe, Ethernet MAC, FIFO, DMA | Verified, optimized, supported | Vendor lock-in, licensing
Third-Party | NWL PCIe, Cadence TIP, Synopsys DesignWare | Advanced features, multi-vendor | Cost, integration effort
Open Source | OpenCores, PULP, LiteX, FuseSoC | Free, transparent, modifiable | Limited support, variable quality
In-House | Custom datapaths, proprietary algorithms | Full control, differentiation | Dev time, verification burden
Integration flow: IP Catalog / Platform Designer → parameterize → generate → connect via bus (AXI/Avalon) → constrain → verify.

## Slide 21
Synthesis & Implementation
Turning RTL into configured silicon
21 / 60

## Slide 22
Logic Synthesis
22 / 60
RTL → Gate-Level Netlist
Synthesis maps HDL code to FPGA primitives (LUTs, FFs, BRAM, DSP). The tool optimizes for area, speed, or power based on directives.
Vivado Synthesis
AMD/Xilinx — incremental synthesis, OOC per module
Quartus Pro
Intel — HyperFlex pipeline optimization, DSE
Synplify Pro
Synopsys — multi-vendor, strong for large designs
Yosys
Open-source — Lattice/iCE40, research, ECP5+
Key decisions: synthesis strategy (Flow_PerfOptimized, Area), retiming, resource sharing, FSM encoding.

## Slide 23
Placement & Routing
23 / 60
1
Opt Design
Logic optimization post-synthesis: constant prop, redundancy removal
2
Placement
Map netlist cells to physical FPGA sites — minimize wire length
3
Physical Opt
Replication, retiming, critical path optimization
4
Routing
Connect placed cells — congestion-aware, timing-driven
5
Post-Route Opt
Final tweaks: hold-time fix insertion, net delay optimization
For large designs: use incremental implementation, pblocks (floorplanning), and out-of-context (OOC) synthesis.

## Slide 24
Timing Closure
24 / 60
Meeting setup & hold requirements across all clock domains.
SDC / XDC Constraints
create_clock — define primary clocks
create_generated_clock — PLL/MMCM outputs
set_input_delay / set_output_delay
set_false_path / set_multicycle_path
set_max_delay for CDC paths
set_clock_groups for async domains
Closure Strategies
Pipeline critical paths (register balancing)
Floorplan with pblocks to reduce wire length
Use phys_opt_design directives aggressively
Clock skew management (BUFG, BUFGCE)
Reduce logic levels: refactor RTL
DSE: sweep strategies automatically

## Slide 25
Pinout & Power Design
Physical I/O planning and power integrity
25 / 60

## Slide 26
Pinout Planning & I/O Design
26 / 60
I/O Bank Rules
Each bank supports specific I/O standards. Cannot mix LVCMOS 3.3V and SSTL 1.2V in the same bank. Plan early.
Pin Locking
Lock critical pins (clocks, transceivers, DDR) first. Use the vendor I/O planner tool before PCB layout.
Differential Pairs
LVDS, SSTL, HSTL require true diff pairs. Verify polarity and pin-pair availability per bank.
SSO / Noise
Simultaneous Switching Output limits per bank. Too many fast outputs → ground bounce. Space and stagger.
Package Migration
Pin-compatible packages allow device upgrades. Design for the footprint family (e.g., FF1156 → FF1760).
PCB Co-Design
Iterate pinout with PCB designer: minimize BGA escape routing, matched-length DDR traces, power plane splits.

## Slide 27
Power Design & Estimation
27 / 60
FPGA power = Static (leakage) + Dynamic (switching activity × capacitance × V² × f)
Early Estimation
XPE / EPE spreadsheets: estimate power pre-design using resource counts and toggle rates
Post-Implementation
Vivado Power Report / PowerPlay: uses actual routing, annotated switching activity (SAIF)
Power Rail Design
Multiple rails: VCCINT, VCCAUX, VCCBRAM, VCCO, MGTAVCC/TT. Use vendor-recommended PMICs (Infineon, MPS)
Thermal Management
Junction temp (Tj) budgets, thermal resistance (θJA), heatsinks, airflow, multi-die thermal stacking

## Slide 28
Power Optimization Techniques
28 / 60
Clock gating — disable clocks to unused logic regions
Block RAM power mode — low-power vs. high-performance BRAM
Dynamic voltage/frequency scaling (DVFS) in SoC designs
I/O standard selection — lower-voltage I/O reduces VCCO power
Partial reconfiguration — load only needed modules at runtime
Transceiver power-down — unused MGTs should be powered off
Synthesis directives — power-optimized synthesis strategies
Toggle rate reduction — gray coding, pipeline balancing
Rule of thumb: Dynamic power typically dominates in large designs. Focus on clock and data toggle rates first.

## Slide 29
Verification & Validation
Ensuring correctness before and after silicon
29 / 60

## Slide 30
Verification Strategy Overview
30 / 60
Verification consumes 60–80% of project effort in complex FPGA designs. A structured approach is essential.
1
Unit / Block
Verify each RTL module independently — focused testbenches, corner cases
2
Integration
Verify interconnected subsystems — bus protocols, data flow, interrupt handling
3
System
Full-chip simulation — end-to-end data paths, boot sequences, error injection
4
Formal
Mathematically prove properties — CDC, connectivity, deadlock freedom
5
Hardware
On-chip validation — ILA, VIO, JTAG debug, lab testing with real I/O

## Slide 31
Simulation & Emulation Tools
31 / 60
Tool | Vendor | Use Case
Vivado Simulator (xsim) | AMD/Xilinx | Integrated, free, good for basic simulation
ModelSim / Questa | Siemens EDA | Industry standard — UVM, CDC, coverage
VCS | Synopsys | High-performance — large SoC verification
Xcelium | Cadence | Multi-language, low-power verification
Verilator | Open Source | Fast cycle-accurate C++ simulation
Cocotb | Open Source | Python-based verification — rapid testbenches
Emulation & Prototyping
Cadence Palladium, Synopsys ZeBu, Siemens Veloce — FPGA-based emulators for SoC pre-silicon SW development at near-real-time speed.

## Slide 32
UVM & Testbench Architecture
32 / 60
Universal Verification Methodology — reusable, scalable verification environment.
UVM Agent
Driver + Monitor + Sequencer per interface — reusable across projects
Scoreboard
Golden reference model — compare expected vs. actual transactions
Sequences
Stimulus generation — random, directed, constrained-random scenarios
Coverage
Functional coverage groups + code coverage → measure verification completeness
For FPGA: UVM adoption varies. Many teams use simpler directed + constrained-random testbenches with Cocotb or SV.

## Slide 33
Formal Verification & Static Analysis
33 / 60
Formal methods mathematically prove design properties without simulation vectors — exhaustive by nature.
CDC Analysis
Spyglass CDC, Questa CDC — identify unsafe clock domain crossings, missing synchronizers
Property Checking
Jasper, Questa Formal — assert/assume/cover properties in SVA, bounded model checking
Connectivity
Verify register map connectivity, bus address decoding, interrupt routing
Equivalence
LEC (Conformal, Formality) — confirm synthesis didn't alter behavior
Lint & Rules
Spyglass Lint, Ascent — coding standard checks, synthesis warnings, naming conventions

## Slide 34
Coverage Metrics & Sign-Off Criteria
34 / 60
Chart: 
| Code | Functional | Formal | Structural
Coverage | 30 | 35 | 20 | 15
Coverage Types
Code Coverage: line, branch, toggle, FSM state/transition
Functional Coverage: user-defined covergroups, cross-coverage
Formal Proofs: assertions proven or bounded to depth N
Structural: connectivity, register access, interrupt paths
Sign-Off Targets
Typical goals: >95% code coverage, 100% functional coverage on critical features, all CDC violations resolved, zero critical lint warnings.

## Slide 35
Hardware Validation & Debug
From bitstream to working hardware
35 / 60

## Slide 36
Bitstream Generation & Configuration
36 / 60
Bitstream Types
Full bitstream, partial reconfiguration bitstreams, encrypted/authenticated bitstreams
Configuration Modes
JTAG, SPI flash, BPI flash, SD card, SelectMAP, ICAP (internal), PS-driven (SoC)
Security
Bitstream encryption (AES-256), HMAC authentication, eFuse key storage, anti-tamper
Compression
Bitstream compression reduces flash size and configuration time (typ. 2–5× reduction)
Multi-Boot
Fallback images, golden/update partitions — critical for remote/field-deployed systems
Partial Reconfiguration: swap logic modules at runtime without full reset — used in multi-tenant, SDR, and adaptive systems.

## Slide 37
On-Chip Debug & Instrumentation
37 / 60
ILA / SignalTap
Insert logic analyzers into the fabric — capture internal signals triggered by conditions
VIO / In-System Sources
Virtual I/O: read/write internal registers in real-time via JTAG
IBERT / Transceiver Toolkit
Eye scan, BER testing, loopback for multi-gigabit transceivers
System Monitor / SDM
On-die voltage, temperature, current sensors — health monitoring
Lab equipment: oscilloscopes, logic analyzers, BER testers, spectrum analyzers — complement on-chip tools for physical-layer debug.

## Slide 38
Hardware Bring-Up Process
38 / 60
1
Power-On
Verify all voltage rails — sequencing, levels, ripple. Check FPGA DONE / INIT_B pins.
2
Configuration
Load bitstream via JTAG. Verify boot from flash. Check configuration time.
3
Clock Validation
Measure reference clocks, PLL lock, jitter. Verify clock distribution.
4
Basic I/O
GPIO toggle test, LED blink, UART console — confirm basic FPGA operation.
5
Memory Init
DDR calibration check, memory BIST, read/write patterns at full speed.
6
Interface Bring-Up
Transceiver link-up, PCIe enumeration, Ethernet link/ping, sensor interfaces.
7
Functional Test
Run application firmware, end-to-end data path, stress testing.

## Slide 39
SoC Software Development Stack
39 / 60
For SoC FPGAs, parallel HW + SW development is critical to schedule.
Bare-Metal / RTOS
Direct register access, interrupt-driven, minimal latency. Xilinx standalone BSP, Intel HWLIB.
Linux / Embedded OS
PetaLinux (AMD), SoC EDS (Intel), Buildroot, Yocto. Device tree configuration for PL peripherals.
Drivers & HAL
Custom Linux drivers for PL IP (UIO, DMA-BUF), AXI-accessible register maps.
Application Layer
User-space apps (C/C++, Python), FPGA manager for runtime reconfiguration, OpenCL/SYCL.

## Slide 40
HW/SW Co-Verification
40 / 60
Verifying the interface between programmable logic and processor subsystem.
Co-Simulation
QEMU + HDL simulator: run ARM firmware against RTL simulation of PL — catches AXI protocol issues early
Virtual Platforms
Vendor virtual platforms (QEMU-based): develop SW before hardware arrives, test boot flow
HW Emulation
Palladium / ZeBu: run full SoC at near-real-time, boot Linux, run SW test suites
FPGA Prototyping
Multi-FPGA prototype boards (Synopsys HAPS, Cadence Protium): real-speed SW development
On-Target Debug
GDB + JTAG, Arm DS, Lauterbach TRACE32: step through SW while monitoring PL signals via ILA

## Slide 41
Production & Deployment
Taking FPGA designs to manufacturing
41 / 60

## Slide 42
Design for Production & Manufacturing Test
42 / 60
JTAG Boundary Scan
Test board-level connectivity using BSDL files — verify solder joints pre-configuration
Built-In Self Test
Memory BIST, transceiver PRBS BER test, loopback checks in production bitstream
Flash Programming
Volume programming: JTAG chains, SPI flash gang programmers, Vivado HW Manager batch mode
Device DNA / eFuse
Unique device ID for licensing, board tracking, and secure boot key injection
Environmental Qual
Temp cycling, HALT/HASS, vibration — especially for aerospace, automotive, industrial
Revision Control
Bitstream version registers, build timestamps, Git SHA in firmware — field traceability

## Slide 43
EDA & Tool Ecosystem Summary
43 / 60
Stage | Tools
Design Entry | Vivado, Quartus Prime, Libero SoC, VS Code + extensions, Sigasi
IP Integration | Vivado IP Integrator, Platform Designer, IP-XACT / Kactus2
Simulation | Questa, VCS, Xcelium, xsim, Verilator, Cocotb, GHDL
Formal / Lint | Spyglass, Jasper, Questa Formal, Ascent Lint
Synthesis | Vivado Synth, Quartus Synth, Synplify Pro, Yosys
Implementation | Vivado P&R, Quartus Fitter, nextpnr (open source)
Debug | ILA, SignalTap, Chipscope, VIO, System Monitor
HLS / AI | Vitis HLS, Intel HLS, Vitis AI, oneAPI, Catapult HLS
Version Control | Git, SVN, FuseSoC, Edalize, CI/CD (Jenkins, GitLab CI)

## Slide 44
Key Takeaways
44 / 60
Modern FPGAs are heterogeneous SoCs — ARM CPUs, AI engines, HBM, and transceivers are first-class citizens.
Verification dominates project effort (60–80%). Invest in testbench infrastructure, formal methods, and coverage early.
Pinout and power planning must start with device selection — late changes are extremely costly.
IP reuse strategy (vendor vs. third-party vs. open-source) is a key architectural decision with long-term impact.
Timing closure on large devices demands floorplanning, incremental flows, and design-for-timing RTL practices.
SoC designs require parallel HW/SW tracks and co-verification — plan for firmware and driver development from day one.
CI/CD for FPGA is maturing — automated synthesis, simulation regression, and bitstream builds reduce risk.

## Slide 45
22
Detailed Development Stages
Workflow view · tools & methods · AI opportunities

## Slide 46
22 Stages at a Glance
46 / 60
Sequence of development activities covered in this section.
1
FPGA high level architecture
2
FPGA pinout design
3
FPGA partition and clock domains
4
Micro architecture design
5
Fast Protocols and transceivers
6
SOC and Soft core design
7
RF design
8
Logic design
9
IP-Core design
10
Static Analysis, Lint & Coding standards
11
Logic Simulation and Verification
12
Formal Verification & Property Checking
13
Design of software and embedded SW
14
Version Control, CI/CD, Build & Regression
15
Design for Test
16
FPGA Design documents and Reviews
17
FPGA Fit (Synthesis + P&R)
18
FPGA Bit Generation
19
Timing Closure
20
Testing POD and software testing
21
ATP Testing
22
Advanced Integration support

## Slide 47
Stages 1–3 · Architecture & Planning
47 / 60
Stage
Tools & methods
AI opportunities
1
FPGA high level architecture
FPGA family/vendor selection; overall FPGA architecture; early resource and power estimation.
• Excel-based power estimation sheets
• Vendor Early Power Estimation (EPE) tools
• MATLAB for DSP modeling
• Engineering judgment from prior designs
▸ Power estimation agent
▸ Utilization estimation agent
▸ FPGA selection agent
2
FPGA pinout design
Map logical signals to physical pins; respect bank voltages, I/O standards, and board constraints.
• Vendor pinout tools (Vivado, Quartus)
• Board schematic cross-reference
▸ FPGA pad design agent
▸ FPGA pad analysis agent
3
FPGA partition and clock domains
Module boundaries, clock domains, and data-flow architecture; clock design per interface and function.
• Architectural sketches
• CDC analysis tools
▸ Partition agent
▸ Clock-domain planner agent

## Slide 48
Stages 4–6 · Micro-architecture & Subsystems
48 / 60
Stage
Tools & methods
AI opportunities
4
Micro architecture design
Translate system-level requirements into module-level architecture.
• MS-Visio / Draw.io
• MS-Word for documentation
▸ Architect agent
5
Fast Protocols and transceivers
Gigabit interfaces: DDR3/4/5, PCIe, CPRI, Aurora, 10/25G Ethernet, JESD204B.
• Vendor protocol IP cores
• Transceiver configuration tools
▸ DDR control agent
▸ Aurora control agent
▸ GETH control agent
▸ PCIe control agent
▸ JESD control agent
6
SOC and Soft core design
SoC system design with AXI interconnect, CPU, external memories, FPGA logic. Tcl-described block design.
• Vivado Block Design
• Vitis
• Questa System Design
▸ TCL design agent
▸ Vivado BD design agent
▸ Vivado BD analysis agent
▸ Quartus QSys design agent
▸ Quartus QSys analysis agent

## Slide 49
Stages 7–9 · RF, Logic & IP
49 / 60
Stage
Tools & methods
AI opportunities
7
RF design
For FPGAs with RF ADC/DAC: design and configure RF converter units.
• Vivado
• Vitis
• Questa System Design
▸ RF configuration agent
▸ RF configuration analysis agent
▸ Xilinx frequency planner agent
8
Logic design
RTL code implementing the microarchitecture; HLS where applicable.
• VS Code + Cline / Continue
• Vitis HLS compiler
▸ RTL agent
▸ HLS agent
▸ Design review agent
9
IP-Core design
Generate vendor cores (FIFO, memory, FFT, filters) and integrate 3rd-party IP.
• CoreGen and vendor IP library
▸ IP-core agent

## Slide 50
Stages 10–12 · Code Quality & Verification
50 / 60
Stage
Tools & methods
AI opportunities
10
Static Analysis, Lint & Coding standards
Code-quality gating: lint, structural and style checks against rule decks.
• Mentor / Spyglass Lint
• vLint
▸ Lint-waiver agent
▸ Coding-standard agent
▸ Rule-deck authoring agent
11
Logic Simulation and Verification
Functional validation via control-logic and vector-driven simulation; UVM/SystemVerilog for advanced testbenches.
• ModelSim / Questa
• CDC tools: vSync, Mentor CDC
• Python / MATLAB for golden vectors
▸ CDC agent
▸ Sim-plan agent
▸ BFM agent
▸ Python simulation agent
▸ Tcl simulation agent
▸ SV agent
▸ UVM plan agent
▸ UVM agent
▸ Sim result analysis agent
12
Formal Verification & Property Checking
Property-based proof for control logic, FSMs, arbiters, CDC paths. Complements UVM.
• Questa Formal
• Synopsys VC Formal
▸ SVA-property generator agent
▸ Cover-point agent
▸ Formal-result analysis agent

## Slide 51
Stages 13–16 · Infrastructure & Process
51 / 60
Stage
Tools & methods
AI opportunities
13
Design of software and embedded SW
SW interfaces, register file, IDD; bare-metal embedded firmware (separate flow).
• MS-Word / Excel for IDD & API
• Vendor embedded-SW IDEs
▸ Memory map design agent
▸ IDD agent
▸ Register agent
14
Version Control, CI/CD, Build & Regression
Git-based version control plus FPGA build/regression for integration and release.
• Git, SmartGit, GitLab, Jenkins
• Make/CMake, Hancho, Python build frameworks
• Vivado/Quartus container images
▸ Git agent
▸ Build-script agent
▸ Regression-dashboard agent
▸ Reproducibility agent
15
Design for Test
Test/debug logic for POD, ATP, and field deployment; operational logging; remote-update support.
• Design documents within microarch and RTL
▸ DFT analysis agent
▸ DFT agent
16
FPGA Design documents and Reviews
FDD, ICD, register description; SRR, PDR, CDR review packages.
• MS-Word, Excel
• MS-Visio / Draw.io
• PowerPoint
▸ SRR agent
▸ PDR agent
▸ CDR agent
▸ FDD agent
▸ ICD agent

## Slide 52
Stages 17–19 · Implementation
52 / 60
Stage
Tools & methods
AI opportunities
17
FPGA Fit (Synthesis + P&R)
Synthesis to target library; placement and routing; timing-driven with constraint files.
• Vivado
• Vitis
• Quartus
▸ Timing-constraint file agent
▸ Placement-constraint agent
▸ Vivado script agent
▸ Quartus script agent
▸ Synth/P&R report analysis agent
18
FPGA Bit Generation
Generate the bitstream / flash image for FPGA programming.
• Vendor IDE bit-gen flow
▸ Bit-gen agent
19
Timing Closure
Verify timing against constraints across PVT corners and all interfaces.
• Vendor STA flows
• Constraint authoring tools
▸ Transceiver constraint file agent
▸ DDR constraint file agent
▸ Pad constraint file agent
▸ Timing results analysis agent
▸ Timing test commands agent
▸ Timing fix proposal agent

## Slide 53
Stages 20–22 · Test & Integration
53 / 60
Stage
Tools & methods
AI opportunities
20
Testing POD and software testing
Full-capability functional test on hardware; POD/ATR documentation; release packaging.
• Test scripts (Python, MATLAB)
• System test application software
▸ POD agent
▸ POD analysis agent
▸ FVD document agent
21
ATP Testing
Production-stage test for unit performance; design team prepares the ATP documentation.
• Production test rigs
▸ ATP documentation agent
▸ ATR analysis agent
▸ ATP debug agent
22
Advanced Integration support
Full-system integration and real-world corner cases; in-system probes for debug and analysis.
• ChipScope / ILA, SignalTap
• Python / MATLAB log analysis
• Application-layer test SW
▸ ChipScope agent
▸ SignalTap agent
▸ ChipScope analysis agent
▸ SignalTap analysis agent
▸ Debug script agent
▸ Result analysis agent

## Slide 54
Design Cycle — Effort & Complexity by Stage
54 / 60
Typical effort distribution and complexity/risk score per stage. Effort sums to 100%; risk is 0 (low) to 5 (high).
#
Stage
% of cycle
Risk
1
FPGA high level architecture
4%
4
2
FPGA pinout design
1%
3
3
FPGA partition and clock domains
2%
4
4
Micro architecture design
6%
4
5
Fast Protocols and transceivers
4%
5
6
SOC and Soft core design
4%
3
7
RF design
2%
5
8
Logic design
17%
3
9
IP-Core design
2%
2
10
Static Analysis, Lint & Coding standards
1%
1
11
Logic Simulation and Verification
22%
5
#
Stage
% of cycle
Risk
12
Formal Verification & Property Checking
2%
3
13
Design of software and embedded SW
3%
3
14
Version Control, CI/CD, Build & Regression
2%
2
15
Design for Test
2%
3
16
FPGA Design documents and Reviews
5%
2
17
FPGA Fit (Synthesis + P&R)
3%
4
18
FPGA Bit Generation
1%
1
19
Timing Closure
6%
5
20
Testing POD and software testing
5%
4
21
ATP Testing
1%
2
22
Advanced Integration support
5%
5
Risk:
1
low
2
3
med
4
5
high

## Slide 55
Design Cycle — Where the Effort Goes
55 / 60
Stages sorted by share of total cycle effort. Verification and RTL dominate; integration and timing closure are next.
5%
10%
15%
20%
11. Logic Simulation and Verification
22%
8. Logic design
17%
4. Micro architecture design
6%
19. Timing Closure
6%
16. FPGA Design documents and Reviews
5%
20. Testing POD and software testing
5%
22. Advanced Integration support
5%
1. FPGA high level architecture
4%
5. Fast Protocols and transceivers
4%
6. SOC and Soft core design
4%
13. Design of software and embedded SW
3%
17. FPGA Fit (Synthesis + P&R)
3%
3. FPGA partition and clock domains
2%
7. RF design
2%
9. IP-Core design
2%
12. Formal Verification & Property Checking
2%
14. Version Control, CI/CD, Build & Regression
2%
15. Design for Test
2%
2. FPGA pinout design
1%
10. Static Analysis, Lint & Coding standards
1%
18. FPGA Bit Generation
1%
21. ATP Testing
1%

## Slide 56
AI Agent Library — Overview
56 / 60
78 proposed agents across the 22 development stages. The next three slides list every agent with its stage and one-line scope.
22
Development stages
78
AI agents identified
9
Agents in Logic Simulation alone
100%
Coverage of the core flow
Stages with the most agent opportunities
11
Logic Simulation and Verification
9
19
Timing Closure
6
22
Advanced Integration support
6
5
Fast Protocols and transceivers
5
6
SOC and Soft core design
5
16
FPGA Design documents and Reviews
5

## Slide 57
AI Agent List · Agents 1–26 of 78
57 / 60
Stages 1 – 10
#
Agent
Stage
#
Agent
Stage
1
Power estimation agent
1. FPGA high level archite…
2
Utilization estimation agent
1. FPGA high level archite…
3
FPGA selection agent
1. FPGA high level archite…
4
FPGA pad design agent
2. FPGA pinout design
5
FPGA pad analysis agent
2. FPGA pinout design
6
Partition agent
3. FPGA partition and cloc…
7
Clock-domain planner agent
3. FPGA partition and cloc…
8
Architect agent
4. Micro architecture design
9
DDR control agent
5. Fast Protocols and tran…
10
Aurora control agent
5. Fast Protocols and tran…
11
GETH control agent
5. Fast Protocols and tran…
12
PCIe control agent
5. Fast Protocols and tran…
13
JESD control agent
5. Fast Protocols and tran…
14
TCL design agent
6. SOC and Soft core design
15
Vivado BD design agent
6. SOC and Soft core design
16
Vivado BD analysis agent
6. SOC and Soft core design
17
Quartus QSys design agent
6. SOC and Soft core design
18
Quartus QSys analysis agent
6. SOC and Soft core design
19
RF configuration agent
7. RF design
20
RF configuration analysis agent
7. RF design
21
Xilinx frequency planner agent
7. RF design
22
RTL agent
8. Logic design
23
HLS agent
8. Logic design
24
Design review agent
8. Logic design
25
IP-core agent
9. IP-Core design
26
Lint-waiver agent
10. Static Analysis, Lint …

## Slide 58
AI Agent List · Agents 27–52 of 78
58 / 60
Stages 10 – 16
#
Agent
Stage
#
Agent
Stage
27
Coding-standard agent
10. Static Analysis, Lint …
28
Rule-deck authoring agent
10. Static Analysis, Lint …
29
CDC agent
11. Logic Simulation and V…
30
Sim-plan agent
11. Logic Simulation and V…
31
BFM agent
11. Logic Simulation and V…
32
Python simulation agent
11. Logic Simulation and V…
33
Tcl simulation agent
11. Logic Simulation and V…
34
SV agent
11. Logic Simulation and V…
35
UVM plan agent
11. Logic Simulation and V…
36
UVM agent
11. Logic Simulation and V…
37
Sim result analysis agent
11. Logic Simulation and V…
38
SVA-property generator agent
12. Formal Verification & …
39
Cover-point agent
12. Formal Verification & …
40
Formal-result analysis agent
12. Formal Verification & …
41
Memory map design agent
13. Design of software and…
42
IDD agent
13. Design of software and…
43
Register agent
13. Design of software and…
44
Git agent
14. Version Control, CI/CD…
45
Build-script agent
14. Version Control, CI/CD…
46
Regression-dashboard agent
14. Version Control, CI/CD…
47
Reproducibility agent
14. Version Control, CI/CD…
48
DFT analysis agent
15. Design for Test
49
DFT agent
15. Design for Test
50
SRR agent
16. FPGA Design documents …
51
PDR agent
16. FPGA Design documents …
52
CDR agent
16. FPGA Design documents …

## Slide 59
AI Agent List · Agents 53–78 of 78
59 / 60
Stages 16 – 22
#
Agent
Stage
#
Agent
Stage
53
FDD agent
16. FPGA Design documents …
54
ICD agent
16. FPGA Design documents …
55
Timing-constraint file agent
17. FPGA Fit (Synthesis + …
56
Placement-constraint agent
17. FPGA Fit (Synthesis + …
57
Vivado script agent
17. FPGA Fit (Synthesis + …
58
Quartus script agent
17. FPGA Fit (Synthesis + …
59
Synth/P&R report analysis agent
17. FPGA Fit (Synthesis + …
60
Bit-gen agent
18. FPGA Bit Generation
61
Transceiver constraint file agent
19. Timing Closure
62
DDR constraint file agent
19. Timing Closure
63
Pad constraint file agent
19. Timing Closure
64
Timing results analysis agent
19. Timing Closure
65
Timing test commands agent
19. Timing Closure
66
Timing fix proposal agent
19. Timing Closure
67
POD agent
20. Testing POD and softwa…
68
POD analysis agent
20. Testing POD and softwa…
69
FVD document agent
20. Testing POD and softwa…
70
ATP documentation agent
21. ATP Testing
71
ATR analysis agent
21. ATP Testing
72
ATP debug agent
21. ATP Testing
73
ChipScope agent
22. Advanced Integration s…
74
SignalTap agent
22. Advanced Integration s…
75
ChipScope analysis agent
22. Advanced Integration s…
76
SignalTap analysis agent
22. Advanced Integration s…
77
Debug script agent
22. Advanced Integration s…
78
Result analysis agent
22. Advanced Integration s…

## Slide 60
Thank You
Questions & Discussion
45 / 60